KSL-1100X Bench-top Muffle Furnace ( 12x8x5") upto 1200 C with  Precision 30 Segments Temperature Controller

Product Description

- Chamber sizes: 438 cubic inches of heating area. ( 12" D x 8" W x 5H" or 7.2 Liter )

- Operation Temperature:  1200 oC max    ( 1200 oC   Max for short time)

- Maximum energy efficiency is achieved by surrounding the chamber with thermal-efficient alumina fiber ceramic insulation

- Heavy duty double layer structure with cooling fan.  Lower temperature in outside case

- Observation widow is built in, which can be changed into gas inlet port by optional inlet tube

- Vent port installed on the top .

- K type  thermocouple installed for immediate use

- Temperature control unit  can be separated from furnace , and make moving at easy

- PID automatic control via current limiting phase angle fired the resistor  with 10 steps programmable

Specifications

| Chamber Cubic Capacity | 438 cubic inch , 7.2 Liter | Replace window by optional tube, you can have gas inlet port |
| --- | --- | --- |
| Chamber Dimensions D xWxH | 11.8 x 7.9 x 4.7" (30 x 20 x 12 cm) |  |
| Volts | 220V single phase 50/60 Hz |  |
| Watts | 3500 W |  |
| Operating Temp Range | 100-1200 oC ( 1200 oC Max for short time) |  |
| Stability at 1000 oC | +/- 0.5 oC |  |
| Uniformity at 1000 oC | +/- 2.0 oC |  |
| Temperature Control | 30 segments programmable via PID control |  |
| Shipping Weight | 110 Lbs |  |
| Overall Dimensions DxHxW | (25" x 21" x 27") |  |

MTI Corporation

860 South 19th Street, Richmond, CA 94804, USA

Tel: 510-525-3070     Fax: 510525-4705      E-mail:  info@mtixtl.com ；      Website:  www.mtixtl.com