MD-10 Precision Mini X-Ray Diffractometer

MD-10 precision mini XRD integrates the state of art technology. It has the compact size as a microwave oven, however it performs phase analysis of powders and solid materials with accuracy and speed comparable to those of full-scale laboratory instruments!  And it is also much cheaper than its larger and heavy rivals. This is the most cost effective solution for R&D and education labs, industrial quality control lab, mobile laboratories for any transportation facility,  and It has been used successfully in materials research, geology, ocean studies, ecology, forensic science, and many other applications. MTI provides one year warranty and free technical support for all customers, as well as extended warranty that makes customer worry free.

Main Features of the MD-10

- Debye-Scherrer geometry, horizontal sample orientation, and spinning sample holder. No goniometer and other precision mechanics to be maintained

- Two incident-beam monochromators improve signal to noise ratio and double the angular range of the detector,

- Sealed-off curved position-sensitive detector with curvature radius 114 mm and Methane-Argon-Xenon gas filling,

- Precise 12-bit ADC provides high resolution and angular measurement accuracy,

- Low power air-cooled X-ray tube with stabilized focus position,

- High-frequency solid-state single block HV power supply

- AC and DC feeding (optional) is possible to operate in lad, car or by a batteries in out side field.

- Compact electronic control and data acquisition system in a single module,

- Real-time data treatment with MS Windows software, and automatically controlled by computer

- Low tube power, radiation protective enclosure and safety interlocks guarantee the safety of the personnel.

- Light weight, small dimension, affordable price, and the low maintenance cost

MTI Corporation

2700 Rydin Road, Unit D, Richmond,  CA 94804, USA

Tel: 510-525-3070     Fax: 510525-4705      E-mail:  info@mtixtl.com       Website:  www.mtixtl.com

Complete Package in delivery

- X-ray Mini Diffractometer MD-10.

- Power cable and parallel cable for connecting XRD with a computer.

- Cuvettes for samples (5 pcs.) and hexahedral screw drivers (2 pcs);

- Control and data acquisition software of the diffractometer and  Software LookPDF for search/match to ICDD databases (in a CD). ( ICDD database not included)

- Operation manual and instruction how to connect MD-10 to your Computer (a Booklet and a CD)

- Brand new laptop computer  installed with windows XP or Window 98  and all MD-10 softwares ready are included. ( Laptop brand name may vary without notice)

- Package dimension: 30" x 28" x 22"

- Shipping weight: 110 lbs

MTI Corporation

2700 Rydin Road, Unit D, Richmond,  CA 94804, USA

Tel: 510-525-3070     Fax: 510525-4705      E-mail:  info@mtixtl.com       Website:  www.mtixtl.com