OTF-1200X-80 Quartz Tube Furnace (80 mm O.D)

With Split Cover and Stainless Steel Vacuum Flanges

OTF-1200X-80 is split-able Tube furnace with Fe-Cr-Al alloy heating element, which can achieve faster heating and cooling rate. The furnace is installed with 80 mm (3.15") O.D quartz tube with a pair of smart stainless steel vacuum sealing flange, 1/2" in diameter vacuum sealing assembly will connect with 1/2" rubber hose, which allow to heat sample in vacuum or flowing gas.  Precision temperature controller can provide 51 segments heating and cooling steps with +/- 1 oC accuracy.

Specifications:

| Power | KW | 2.5 |
| --- | --- | --- |
| Voltage | V | AC 208-240 Single Phase, 50/60 Hz |
| Max. Temperature | oC | 1200 (<1 hour) |
| Continuous Temperature | oC | 1100 |
| Max. Heating Rate | oC /min | <= 20 |
| Suggested Normal Heating Rate | oC /min | 10 |
| Tube Size and Materials | mm | OD: 80; ID: 72; Length: 1000, 80mm Quartz tube ( included ) |
| Hot Zone Length | mm | 440 |
| Constant Temperature Zone |  | 120 (+/- 1 oC) @ 400-1200 oC |
| Temperature controller |  | PID automatic control via current limiting phase angle fired the resistor with 30 steps programmable |
| Temperature Accuracy | oC | +/ - 1oC |
| Vacuum Level ( by a mechanical pump ) | torr | 0.1 ( vacuum pump 's pressure can reach < 0.0001 torr ) |
| Heating Element |  | Fe-Cr-Al Alloy doped by Mo |
| Dimension | mm | 550 x 380 x 520 |
| Net Weight | Kg | about 60 |
| Warranty |  | One year limited on all electronic parts, not including quartz tube |
| Shipping package size after crating | inch | 45x45x35 |
| Shipping weight | lbs | 200 |

MTI Corporation

860 South 19th Street, Richmond, CA 94804, USA

Tel: 510-525-3070     Fax: 510525-4705      E-mail:  info@mtixtl.com       Website:  www.mtixtl.com