SWGL1700X Dual Zones Tube Furnace

SWGL-1700X is 3" dia. dual zones tube furnace. Each heating zone is 12" in length and controlled by 10 segments digital temperature controller independently.  One zone is heated by MoSi2 elements up to 1700 oC, and another zone is heated by SiC element up to 1300oC. So the tube furnace can create various thermal gradient by adjust two zone temperature. It is an excellent furnace to prepare functional materials under thermal gradient, and also can be used for epitaxial film growth by CVD or PVD with a vacuum system

Specifications:

| Power | KW | 5 KW |
| --- | --- | --- |
| Voltage | V | AC 220-240 Single Phase, 50/60 Hz |
| Max. Temperature | oC | Zone one:` 1300 oC , Zone two: 1700oC |
| Tube Size and Materials required | mm | Alumina Tube 2" dia. x 48" Length required ( not included ) 40 mm dia. or 60 mm dia. tube setup is available upon request at same cost |
| Temperature Controllers |  | Two Digital Controller, and each has 10-segement programmable |
| Temperature Accuracy | oC | +/ - 1 oC |

You may choose our high purity alumina tube as liner (not included), and our vacuum seal kit to fit the tube and run the furnace under vacuum or gas flow.

MTI Corporation

860 South 19th Street

Richmond, CA 94804, USA

TEL: (510)525-3070     FAX: (510)525-4705

Web site:  www.mtixtl.com   E-mail: info@mtixtl.com