PROFESSIONAL INVERTED METALLURGICAL MICROSCOPE WITH POLARIZING + 3.0 MP DIGITAL CAMERA 40X-1600X, EB-XJM413H

The XJM413 inverted, metallurgical microscope system provides superb optics, built-in polarization capabilities, color filters and up to 1000X magnification with a USB digital image camera. It offers 3.0 M pixel resolution and is compatible with Windows 98/2000/XP. Its built-in reduction lens gives the same field of view images on your PC screen as that seen through eyepieces. Using the user-friendly software, you can edit microscope images on your computer or email them to your supervisor or colleagues. You can make real time video or save microscope images as BMP, TIFF, JPG, PICT, PTL or other files. You can also measure length, angle, area and etc. across the images.   This microscopy system is perfect for metallurgical labs and foundries for silicon wafer inspection, integrated circuit examination, quality control and R&D applications.

Specifications:

- Head: 30o inclined trinocular.

- Three sets of Eyepieces: WF10X/22 and WF10X/22 with reticule 0.1mm.

- Objectives: infinitive Plan Achromatic objectives, 4X, 10X, 20X & 40X for metallurgical applications and infinitive Plan Achromatic objectives, 40X &100X, for biological applications.

- Polarization System: built-in polarizer and analyzer, which is rotatable 360o and  can be slided in / out of the optical path

- Diaphragm: Epi-illuminator with Iris aperture diaphragm and iris field diaphragm.

- Stage: double layer mechanical stage with size 185X150mm, and 75x50 mm travel distance range.

- Illumination Systems: 12V30W T-H lamp for metallurgical applications (intensity adjustable, lamp centering adjustable) and built-in 12V20W T-H lamp for biological applications (intensity adjustment).

- Filter: Green, blue and yellow

- Vertical Photo/Video Port: 23mm universal/standard photo tube (100%-0% or 20%-80%).

- Power Supply: AC85V-230V Adjustable brightness CE certified for worldwide use

- Spare bulb, fuse and a bottle of immersion oil are included.

- 3.0MP digital camera head and software are included. Compatible with Windows 2000/me/XP/Visita

- Weight: 50 lbs.

- Packages size:  40x47x50 cm

MTI Corporation

860 South 19th Street, Richmond,  CA 94804, USA

Tel: 510-525-3070     Fax: 510525-4705      E-mail:  info@mtixtl.com       Website:  www.mtixtl.com